# Discovery 2 Chapter 3 Quiz

- What three types of network documentation does a technician need to complete before designing a new network? (Choose three)

  - cut sheet

  - inventory sheet

  - site survey report

  - standards evaluation

  - topology maps

  - upgrade initiative

- What should the on-site technician do immediately after completing the site survey?

  - begin scheduling the work for the network upgrade

  - order the networking devices and software required

  - review the survey results with the network designer

  - review the survey results with the customer to ensure accuracy

- Which three steps must be completed before implementation of the new network can begin? (Choose three)

  - The network is brought into a production environment.

  - Projected designs and costs are compared with actual deployment.

  - Prototypes are created and tested.

  - An Analysis Report is generated.

  - The design is approved by the customer.

  - The operation of the network upgrade is monitored.

- What are two characteristics of horizontal cabling?  (Choose two)

  - It terminates at a face plate in the user work area.

  - It connects directly to a switch or router in the MDF.

  - It terminates at a patch panel in the IDF or MDF.

  - It connects two networking devices located in different IDFs.

  - It connects the PC to the face plate.

- When designing a structured cable project, why is it important to obtain an accurate floor plan? (Choose three)

  - to design the Layer 3 addressing

  - to share the conduit with existing electricial wiring

  - to identify possible wiring closet locations

  - to determine the number of host devices needed

  - to avoid areas with electrical equipment or wiring

  - to estimate how much cable will be required

- Match the cable type on the top to the appropriate description on the bottom.

  - patch cable

  - horizontal cable

  - vertical cable

  - cable-containment system

  - cable from the IDF to the MDF in the organization’s backbone area

  - a series of trays and straps used to guide and protect cable runs

  - short cable from the computer to the wall plate in the user work area

  - cabling from the wall plate to the IDF in the distribution area

- Why is it important to consider the size of failure domains when upgrading a network?

  - Creating large failure domains reduces the number of IP broadcast domains.

  - Small failure domains reduce the number of users affected when a network device malfunctions.

  - Large failure domains usually improve the network reliability and reduce downtime.

  - It requires fewer networking devices to create small failure domains than large ones.

- Why would a managed-service customer want to have an SLA with the ISP?

  - to ensure that equipment ordered from vendors is delivered on time

  - to provide extended warranties for customer-installed networking equipment

  - to guarantee customer premises wiring meets all required standards

  - to have a written agreement of what services the ISP will provide

- Where would the on-site technician record information about the brand, model, and operating system of the hosts and networking devices installed on the network?

  - topology map

  - inventory sheet

  - office floorplan

  - analysis report

- ISP is recommending a Cisco 1841 ISR to upgrade a small business customer LAN.  Why is an ISR a good choice for a small business customer? (Choose two)

  - An ISR often costs less than a stand-alone router and a LAN switch solution.

  - The ISR eliminates the need for on-site email or web servers.

  - ISRs combine routing, switching, and wireless capabilities in a single device.

  - ISRs are a good choice because small businesses usually do not require firewall security.

  - Because the ISR features are limited to routing and switching, they are easier to configure.